## Slide 1: Energy Storage and Transport
Modeling example

## Slide 2: The model development cycle
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implemen-tation
Validation & verification
Reflection
Analyze the context and define an objective for modeling. Which purpose can a model serve in the project?
Perform research to understand the physical phenomena that play a role in the project. How do they relate to the modelling objective?
Select which phenomena are essential to include and which may be neglected. Which simplifications and assumptions can be made?
Define and combine the mathematical relations that describe the physical phenomena and apply the selected simplifications.
Create the model which uses the mathematical relations to predict (an) outcome(s) based on given inputs.
Validate: does the model solve the right equations?
Verify: does the model solve the equations correctly?
Is the modelling objective met? What are the uses and limitations of the model?
How can it be improved?
Iterate steps when appropriate

## Slide 3: Energy Storage and Transport
Large off-shore wind farm, transporting electric energy to a hydroelectricity dam using high-voltage transmission lines.
Topic of this lecture: Model development for the transmission lines
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection
Supply: 100 x 10 MW
Transport to storage
Storage
100-mile transmission line

## Slide 4
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection
The model as a black box
The transmission line model should provide a relation between:
  Input: power supplied by the turbines
  Output: power delivered to the storage
Transmission system model

## Slide 5: Modeling questions
How much energy is lost in the transmission lines?
How do these losses depend on the transport system parameters?
  Length of the transmission lines
  Electricity transport voltage and power
  Type of transmission cables
  Type of transformers
  Etc.
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection

## Slide 6: What are typical losses?
Example from literature:
A 100 mi (160 km) span at 765 kV carrying 1000 MW of power can have losses of 0.5% to 1.1%.
A 345 kV line carrying the same load across the same distance has losses of 4.2%.
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection
100 mile
1000 MW @ 765 kV
1000 MW @ 345 kV
 Loss: 0.5-1.1 %
 Loss: 4.2 %

## Slide 7: Why is a higher voltage better?
Transported power = voltage [V] x current (A):
Power losses = resistance [Ohm] x current (A)^2
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection
Best to transport energy at a low current
Given a fixed transport power, the current can be lowered by increasing the voltage

## Slide 8: What causes the losses?
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection
Joule heating
resistance of wires
Dependent on properties of cables and power current
 Assumption: main source of loss
Leakage
to ground
Minimal in a correctly designed system
 Assumption: can be neglected
Corona losses
air ionization
Only relevant when voltage exceeds the corona threshold
Dependent on weather conditions and temperature
 Assumption: can be neglected
Inductance
caused by magnetic field
Only relevant for alternating current
 Assumption: direct current is used
Transformer losses
efficiency of transformer
Expected to be small, but significant
 Assumption: take into account

## Slide 9: The energy flow diagram
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection
Transmission system model
Transf up
Transf down
Transm lines
The structure of your model:
  How do the sub-components connect ?
  Where are the losses?

## Slide 10: The transmission lines
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection
Cables
Joule heating losses in Watts [W]:
  R: resistance in Ohm [
  I: electric current in Amperes [A]
Wire resistance:
  L: Length of cable
  R’: Resistance per unit length
Power balance:

## Slide 11: Does it make sense?
Modelling objective
Physical phenomena
Model selection
Mathematical relations
Implementation
Validation & verification
Reflection
  ACSR cable spec sheet:
100 mile
1000 MW @ 765 kV
1000 MW @ 345 kV
 Loss: 0.5-1.1 %
 Loss: 4.2 %

## Slide 12: The transformers
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection
Heat losses scale with the input power [W]:
  a: loss coefficient [
Loss coefficient is related to efficiency:
Power balance:
Transformer

## Slide 13
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection
Transmission system model
Transfup
Transf down
Transm lines
Putting the model together

## Slide 14: Checking the result
Modelling objective
Physical phenomena
Model selection
Mathematical relations
Implementation
Validation & verification
Reflection
Transmission system model
Transfup
Transf down
Transm lines
+

## Slide 15: Does the result make sense?
Estimating parameters from spec sheets:
  High-voltage transformer:
  ACSR cable:
Losses at 1000 MW and 765 kV:
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection

## Slide 16: The transport function block
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection

## Slide 17: The transport function block
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection
Effective loss parameter in baseline implementation
Inside the "Transport from supply" block:
preprocessing.m

## Slide 18: The implementation of the model
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection
Inside the "supplyTransport" function block:
Not of the form same form due to quadratic dependence on the input power.
Requires new implementation of the Matlab function.

## Slide 19: The implementation of the model
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection
Inside the "supplyTransport" function block:

## Slide 20: The transport function block
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection
Inside the "Transport from supply" block:

## Slide 21: The physical input parameters
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection
preprocessing.m

## Slide 22: Debugging
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection
Study the error message to understand what is wrong.
If you cannot find the bug, revert to the version that worked, and then make step-by-step changes.
Create test cases to track the bug.

## Slide 23: The physical input parameters
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection
preprocessing.m

## Slide 24: Do the results make sense?
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection
Standard output does not properly visualize the change.
Add additional output to assess model change.

## Slide 25: Do the results make sense?
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection
Losses around 2%
Dominated by transformers because of low power
Additional testing at high powers needed

## Slide 26: What can the model do?
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection
Provide estimate of power losses in DC transmission lines
Model allows variation of:
  Length of transmission line
  Resistance of lines (material property)
  Voltage in transmission line
  Transformer efficiencies
Results correspond well with literature observations

## Slide 27: What can be improved?
Modelling objective
Physical phenomena
Model selection
Mathematical elaboration
Implementation
Validation & verification
Reflection
Further validation by considering higher powers
Extend to AC transmission lines by including inductance in the model
Add an improved model for the transformers

## Slide 28: Energy Storage and Transport
Modeling example